## Slide 1: Using Topaz – Set up
# set up your directories
$ mkdir topaz
$ mkdir topaz/data
$ mkdir topaz/data/raw
$ mkdir topaz/data/processed
$ mkdir topaz/saved_models

## Slide 2: Using Topaz – Preprocessing
# Combination of binning and normalization. You can either copy your raw data into the topaz/data/raw directory or just tell topaz where your raw data currently is. Below, I assume it’s in Leginon.
# use “topaz preprocess –h” to see all of the options
# “-s 4” indicates binning the micrographs by 4. It’s the default
$ cd topaz
$ topaz preprocess /gpfs/leginon/USERNAME/SESSION/rawdata/*DW.mrc -s 4 --o data/processed/ -t 23
# You’ll end up with a bunch of .tiff files in the data/processed/ directory
# Might take a while (>60 minutes) if you have a lot of micrographs
Raw micrographs
Bin
Output
directory
Processes

## Slide 3: Using Topaz – Input files
# First you need a .star file with the particle picks you want to train your neural network with. How many picks depends on the protein and the quality of the data. A nice, big particle in good ice might only need 100-200 picks. Something small might need 2,000. Make sure the picks are accurate! Put the .star file in your topaz directory.
$ module load anaconda/2
$ python /home/mrapp/topaz_input_prep.py data/processed/*.tiff particles.star -oi all_images.txt -of all_filtered_images.txt -oc all_coord.txt
# For the Appion devs, topaz_input_prep.py is just a merger of generate_image_list.py, filter_images.py, and star_to_coordinates.py from the Topaz github.
Input processed micrographs
Input
star file
Name of output
image list
Name of output
Filtered image list
Name of output
coordinate list

## Slide 4: Using Topaz – Input files
# Now you have to scale the coordinates down to match the preprocessing step.
# The scale is 1 over whatever you entered for preprocessing. So binning by 4 will be 0.25
$ topaz scale_coordinates all_coord.txt -s 0.25 -o all_scaled_coord.txt
Input coordinates
Scale
(<0)
Name of output
scaled coordinate list

## Slide 5: Using Topaz – Input files
# The input files are now split in two – a list of particles for training and a list for testing
# Use around 2/3 of your micrographs (assuming a pretty even number of picks in each) for training and 1/3 of them for testing. Below, I assume 30 micrographs, so 10 for testing.
# the following files will be generated…
all_filtered_images_test.txt all_filtered_images_train.txt
all_scaled_coord_test.txt all_scaled_coord_train.txt
$ python /gpfs/sw/topaz/scripts/train_test_split.py --images all_filtered_images.txt --targets all_scaled_coord.txt -n 10
Input filtered image list
Input scaled coordinates list
# of images
for testing

## Slide 6: Using Topaz – Training
# Now you’re ready to train!
# First, qsub into a GPU node. Topaz only ever uses 1, but having access to multiple will let you vary parameters and train multiple networks at the same time to see what works best. Make a directory to store your models. There are a lot of parameters to change in Topaz and it is definitely worth playing with them. Each time you change something, you’ll get a new model, so make a new directory each time, preferably naming it something that tells you what parameters you used. The name will make sense after the next few slides.
$ qsub -q gpu1
$ cd /PATH/TO/topaz/
$ mkdir saved_models/radius3_pi035_conv63

## Slide 7: Using Topaz – Training
# First you need to point Topaz to your training and test .txt files (use scaled coordinate and filtered image lists)
Input images for training
Input images for testing
Input coordinates for training
Input coordinates for testing
$ topaz train --train-images all_filtered_images_train.txt --test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt

## Slide 8: Using Topaz – Training
# Then we specify the pi parameter. Pi is the expected fraction of positive pixels, so pixels that correspond to a protein. Somewhere around 0.03 to 0.05 works.
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035
Pi value
(~0.03 – 0.05)

## Slide 9: Using Topaz – Training
# Then we set the radius. The radius parameter specifies “how many pixels around a labeled particle coordinate should be treated as positive.” It should always be less than the real radius. Tristan recommends somewhere between 3 and 4. I’ve gotten good results up to 15. Sometimes topaz will fail if the radius value is too high. Not sure why.
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035 --radius 3
Radius
(~3-15)

## Slide 10: Using Topaz – Training
# Topaz has 4 model architectures. I have no idea what the differences are, but it’s worth seeing which one works best. The options are resnet8, conv127, conv63, and conv31. Below I’ve used conv63 which did the best on my test dataset without taking forever.
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035 --radius 3 --model conv63
Neural network architecture
(conv31, conv63, conv127, resnet8)

## Slide 11: Using Topaz – Training
# By default, Topaz will run through 10 epochs, generating a model for each one as a .sav file. Give it a generic prefix.
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035 --radius 3 --model conv63 --save-prefix saved_models/radius3_pi035_conv63/model
Generic prefix for model output files
(_epochX.sav will be added to the end, where X is the epoch number)

## Slide 12: Using Topaz – Training
# Topaz will generate a .txt file with the results of training and testing. Give it a name
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035 --radius 3 --model conv63 --save-prefix saved_models/radius3_pi035_conv63/model -o saved_models/radius3_pi035_conv63/model_training.txt
Name out output model training file

## Slide 13: Using Topaz – Training
# Set the number of worker processes for data augmentation. Not sure what it should be.
$ topaz train --train-images all_filtered_images_train.txt
--test-images all_filtered_images_test.txt --train-targets all_scaled_coord_train.txt --test-targets all_scaled_coord_test.txt --pi 0.035 --radius 3 --model conv63 --save-prefix saved_models/radius3_pi035_conv63/model -o saved_models/radius3_pi035_conv63/model_training.txt --num-workers 8
# Now run the command. It might take a while. For me, it took between 30 and 60 minutes on 1 GTX 1080 Ti
Number of processes

## Slide 14: Using Topaz – Evaluating the model
# Topaz generates a .txt file that reports how well the network predicted the particle picks in your test set. We are interested in the AUPRC (Area Under the Precision Recall Curve). The important things to know are 1) it’s not comparable to different training and test datasets but 2) it is internally consistent, so higher is better
$ cd saved_models/radius3_pi035_conv63
$ awk ‘$3 ~ /test/ {sum+=$9} END {print sum/10}’ model_training.txt
# This will report the average AUPRC for the 10 (by default) epochs. Run the following command to see the AUPRC for each epoch. It’s the last column.
$ awk ‘NR==1 || $3 ~ /test/’ model_training.txt

## Slide 15: Using Topaz – Evaluating the model
# Now go back and vary your radius, pi, and model parameters to get the highest AUPRC you can. It might be good to get a few GPUs and do it simultaneously.

## Slide 16: Using Topaz – Extracting particles
# Once you’ve got a model that you’re satisfied with, you’ll apply it to the rest of your preprocessed micrographs. Specify a radius that corresponds to the radius of your particle in the binned image. E.g. if the particle diameter is 15 pixels, use a radius of 7.
# This might take a couple of hours. Go get some coffee.
Processed micrographs to be picked
Particle radius
(just over half the real radius)
Neural network epoch to apply
(one with highest AUPRC)
Name for output particle list
$ topaz extract ./../../data/processed/*.tiff -r 7 -m model_epoch10.sav -o predicted_particles_all.txt

## Slide 17: Using Topaz – Scaling particles
# Now you have to scale your particles back up using the same command as before, but this time the –s argument will be your scaling factor from preprossing.
$ topaz scale_coordinates predicted_particles_all.txt -s 4 -o predicted_particles_all_scaled.txt
Input particle list
Binning used in preprocessing
Output named for scaled up particle list

## Slide 18: Using Topaz – Getting to a .star file
# Time to turn your topaz .txt file into a star file.
$ topaz coordinates_to_star predicted_particles_all_scaled.txt --image-ext .mrc --voltage 300 --spherical-aberation 2.3 --amplitude-contrast 0.07 --detector-pixel-size 5 --magnification 47147.57190 > predicted_particles_all.star
# This will contain every single particle predicted by Topaz, and there will be a lot
Input scaled up particle list
Micrograph extension
Microscope parameters
Name for output star file

## Slide 19: Using Topaz – Getting to a .star file
# Each particle Topaz predicts is assigned a score. You can threshold your .star file by that score. A score of 0 is a good place to start. Increasing the score will limit you to particles Topaz is more confident are real particles. Lowering it will get you more particles that Topaz is less confident about. The command will tell you how many particles you started with and how many you ended up with once the threshold was applied.
$ topaz star_particles_threshold predicted_particles_all.star -t 0 -o predicted_particles_0.star
Input star file
Threshold value
Output thresholded star file

## Slide 20: Using Topaz – Getting to a .star file
# Currently, Topaz includes its particle score in the .star file under the _rlnParticleScore label, which will cause Relion to spit out an error when you go to extract. The easiest way around it is just to open the .star file and delete the label. Use your favorite text editor.
$ more predicted_particles_0.star
data_images
loop_
_rlnMicrographName #1
_rlnCoordinateX #2
_rlnCoordinateY #3
_rlnParticleScore #4
_rlnVoltage #5
_rlnSphericalAberration #6
_rlnAmplitudeContrast #7
_rlnDetectorPixelSize #8
_rlnMagnification #9
Delete this line

## Slide 21: Using Topaz – Done!
# Now you’re ready to extract your particles in Relion and go on processing with your favorite program.
# Topaz also has some scripts for converting to and from .box files, but I haven’t used it yet so can’t speak to its usability.
# If you feel like you need more particles, go back to the star thresholding step and set –t to a lower number then re-extract. Hopefully one day that particle score can be used in other processing packages.
# Topaz should be integrated into Appion soon!